## Slide 1: حل تمرین مدار منطقی

## Slide 2: 1. مروری بر درس

## Slide 3: Setup Time, Hold Time and Propagation Delay
Setup time:
  D input must be stable for a certain amount of time BEFORE the active edge of clock
Hold time:
  D input must be stable for a certain amount of time AFTER the active edge of the clock
Propagation Delay (Clock-to-Output):
  From the time the clock changes to the time the output changes
Propagation Delay (Data-to-Output):
  From the time the data changes to the time the output changes
  Mainly defined for latches

## Slide 4: Setup & Hold Time and Propagation Delay
Setup and hold times for a rising edge-triggered D flip-flop
tpLH may be different than tpHL
tp clock-to-output vs. tp D-to-output

## Slide 5: Timing Requirements
Determination of minimum clock period
Assume:
tco= 5 ns
tp,inv = 2 ns
tsu= 3 ns

## Slide 6: 2. نمونه سوالات